## Slide 1: Columbia River Basin Water Supply Forecasting
AI Delinquents | ESSD AI Competition 2025 Cameron Bracken, Stefan Rose, Matt Sturtevant, Amanda Lawter, Jana Simo

## Slide 2: The Problem
Predict April–September naturalized streamflow volume at The Dalles, OR

## Slide 3
Why it matters
Snowmelt-driven Columbia Basin supplies hydropower, agriculture, and municipal water for the Pacific Northwest
Forecasts issued each April 1 inform reservoir operations for the coming summer
Existing NRCS/NWRFC forecasts use statistical methods — can ML improve on them?
Success criteria
Metric | Target
NSE | > 0 (beat mean)
RMSE | < 8,488 kcfs-days (beat climatology)
Skill score | > 0 vs climatology
Target variable: Apr–Sep naturalized flow volume (kcfs-days) Forecast window: Conditions known by April 1
Notes: Stefan or Cameron — set the scene. The Dalles is the most important control point on the Columbia River. Naturalized flow removes reservoir regulation effects so we’re modeling the basin’s actual water supply, not what operators decided to release. Our success bar was simply: beat the climatology (historical average) on the held-out test set.

## Slide 4: Data & Key Predictors
Four data sources → 7 features
Feature | Source | r
Apr 1 SWE anomaly (%) | NRCS SNOTEL (16 stations) | 0.79
Jan–Mar mean flow (cfs) | BPA natural flow | 0.56
Oct–Mar volume (kcfs-days) | BPA natural flow | 0.55
DJF Nino3.4 | NOAA PSL | −0.46
DJF PDO | NOAA PSL | −0.45
DJF PNA | NOAA PSL | −0.40
34 complete water years (WY 1985–2018)
Snowpack is the dominant predictor. La Niña years (blue) consistently produce higher runoff at a given SWE level than El Niño years (red).
Notes: Amanda or Jana — highlight that we used naturalized (BPA modified) flow, not observed regulated flow. The scatter plot shows the two key signals: snowpack (r = 0.79) and ENSO phase. La Niña winters enhance Pacific Northwest precipitation; El Niño suppresses it — the vertical spread at any SWE value reflects that teleconnection. This guided our feature engineering choices.

## Slide 5: Methodology

## Slide 6
Leakage prevention: Temporal split only — no future data used in training. Hyperparameter tuning done inside LOYO folds on training years only. Test set locked until final evaluation.
Notes: Matt — walk through the pipeline. The key design decision is the temporal split: we held out the 6 most recent years (2013–2018) as a true holdout. Leave-One-Year-Out cross-validation within the training set tuned XGBoost hyperparameters without ever seeing the test years. This mirrors how operational forecasts work — you never have future data.

## Slide 7: ML Results
MLR closely tracks observed volumes across 34 years. XGBoost prediction intervals (blue band) provide uncertainty quantification but undercover at ~67%.
Test set performance (WY 2013–2018)
Model | NSE | RMSE
Climatology | −0.03 | 8,488
MLR | 0.77 | 4,034
XGBoost | 0.46 | 6,170
MLR outperforms XGBoost — expected with n=34. Linear relationships dominate at this sample size; XGBoost’s nonlinear capacity is a liability without more data.
LOYO CV NSE: MLR = 0.69, XGBoost = 0.44 — consistent with test set, no overfitting signal.
Notes: Cameron — the headline finding is that the simple linear model won. This is physically reasonable: Apr 1 SWE is linearly correlated with spring runoff (r = 0.79). XGBoost would likely outperform MLR with a longer training record. The prediction intervals from XGBoost quantile regression have ~67% coverage vs the 80% target — the model is somewhat overconfident.

## Slide 8: Interpretability
Antecedent flow conditions (Jan–Mar Q, Oct–Mar volume) top the importance ranking — reflecting that early-season runoff integrates temperature, precipitation, and snowmelt signals that are only partially captured by Apr 1 SWE alone.
What the model learned
Antecedent flow (Jan–Mar, Oct–Mar) ranked highest — captures early snowmelt and baseflow that SWE alone misses
Apr 1 SWE still central — both raw inches and anomaly % appear, reflecting scale and departure from median
Climate indices (PDO, PNA, Nino3.4) provide secondary modulation — the ENSO scatter plot pattern is reflected here
Physical check: Rankings align with operational forecaster intuition. No spurious features.
Notes: Stefan — the feature importance is physically interpretable, which is a good sign. Operational NRCS forecasters weight snowpack heavily but also use antecedent flow as a quality check on snowpack accumulation. The fact that Jan–Mar flow tops the list makes sense: by Jan–Mar you have more current information than the Oct–Mar integral.

## Slide 9: LLM Benchmarking Approach
Can a general-purpose LLM predict streamflow volume from a text description of predictors?

## Slide 10
Prompt design
You are a hydrologist forecasting seasonal water supply. Given conditions for a water year, predict the total April–September naturalized streamflow volume. Rules: - Return ONLY: {"prediction_kcfs_days": <number>} - Typical range: 28,000–71,000 kcfs-days Water year 2013 conditions: - Apr 1 SWE: 25.2 inches (−12% vs median) - DJF Nino3.4: −0.43 (La Niña) - Jan–Mar mean flow: 103,131 cfs ...
v1: Zero-shot (format constraint only)
v2: 3 few-shot examples (dry/median/wet training years)
Three endpoints tested
Model | Size | Port
Phi-3.5-mini-instruct | ~3.8B | 8000
Phi-mini-MoE-instruct | ~7B | 8001
gemma-3-12b-it | 12B | 8002
Same test split as Week 3 WY 2013–2018, n = 6
Parse success: 100% Strict JSON format worked on every query
Notes: Matt or Amanda — the key challenge here was adapting a classification tutorial to a regression task. We had to design the prompt to elicit a specific numeric prediction, not a label. The 100% parse success rate validated the prompt format design. We tested both zero-shot and few-shot, then selected the better-performing version per model for the final benchmark.

## Slide 11: ML vs LLM: Results

## Slide 12
Model | Type | NSE | RMSE
MLR | ML | 0.77 | 4,034
XGBoost | ML | 0.46 | 6,170
gemma-3-12b-it | LLM | 0.33 | 6,817
Phi-3.5-mini | LLM | 0.12 | 7,824
Phi-mini-MoE | LLM | −0.57 | 10,472
Key finding: All LLMs showed compressed prediction variance — clustering near climatology regardless of input
WY 2017 (wet): MLR predicted 57,557 vs observed 57,104. Phi-mini-MoE predicted 40,000.
Phi-mini-MoE was the only model worse than predicting the mean every year
Notes: Cameron — this is the headline slide. The left panel of the figure shows the flat-line behavior of the Phi models — they barely respond to the strong 2017 signal. Gemma is the best LLM by far (12B parameters vs ~4-7B for Phi), suggesting model scale matters more than prompt engineering for this task. Note that gemma still beat XGBoost — so a large general LLM can partially compete with a tuned ML model.

## Slide 13: Limitations & Risks
Model limitations
Small training set (n=28): XGBoost constrained by data volume; MLR dominates
Short test window (n=6): Single anomalous year shifts NSE by ±0.1–0.2
XGBoost PI undercoverage: ~67% vs 80% target — overconfident intervals
No future climate: Models assume stationarity; climate change may shift the SWE–runoff relationship
WY 2015 — hardest year
Record drought (−51% SWE, strong El Niño). Every model missed it. True: 31,185; Best prediction: Phi-mini-MoE at 30,000 (likely coincidental).
LLM-specific limitations
Regression to the mean: LLMs anchor near climatology — they lack a learned feature-to-volume mapping
Numeric reasoning: Numbers are tokens, not quantities — proportional scaling to extremes is unreliable
Not fine-tuned: General-purpose models with no exposure to Columbia Basin hydrology
Prompt version confound: Zero-shot was better for Phi-3.5-mini; few-shot better for larger models — comparison not fully controlled
Next steps: Longer training record (BPA extends to WY 1929), fine-tuned LLM, sub-basin disaggregation
Notes: Jana or Stefan — be honest about limitations. The WY 2015 miss is the most important failure case operationally — that year caught everyone off guard, including NRCS. The LLM limitation around numeric reasoning is a fundamental one, not a prompt design problem. Domain-specific fine-tuning would likely close much of the gap.

## Slide 14: What We Learned
Modeling Simple models win with small data. MLR outperformed XGBoost because 34 water years isn’t enough to exploit nonlinear interactions. Model selection must match sample size.
Data Naturalized flow data was essential — regulated flow would have added noise from operator decisions. Feature engineering (SWE anomaly, DJF indices) added more predictive value than raw inputs alone.
ML vs LLM LLMs are impressive generalists but poor tabular regressors. Parse reliability was perfect; prediction accuracy was not. Model scale mattered more than prompt engineering.
From mistakes WY 2015 exposed our biggest gap: no model handled extreme out-of-distribution inputs well. XGBoost had the worst miss on 2015 despite the best CV score — a reminder that CV metrics don’t guarantee robustness to extremes.
As a team Git branching by week kept deliverables organized across 5 members with different expertise. Reproducibility (pixi environments, seeded models, locked dependencies) paid off when re-running analyses. AI-assisted coding accelerated development but required careful domain review at every step.
Notes: All team members — go around the room for this slide, each person speaking to one bullet. This is the culmination slide. Emphasize that the most valuable learning wasn’t the metrics — it was the process: designing a reproducible pipeline, making deliberate modeling choices, and honestly documenting where things failed.